Motherboard All In One 5SFV

COM A		3F8 / IRQ4	25 pol. fun.link

COM B		2F8 / IRQ3	9 pol.	Data Print

COM C		3E8 / IRQ3	9 pol.	SMT3 (serial Touchscreen Controller)

COM D		2E8 / IRQ10	9 pol.	Modem (Photo Play MASTERS)

Starting BIOS Menu:

Connect a PC keyboard to the 5-pin DIN-keyboard jack and switch on the unit. During the funworld logo, press the “Del”-key. The BIOS menu appears. Get to the funworld setting via “Load setup defaults” ( press “Z” key for Yes )

Standard CMOS Setup:

Date (mm:d:yy) 	    : 		Mon, Jun 08 1998

Time (hh:mm:ss)	    : 	13   :   58   :   52

HARD DISKS 	           TYPE 	     SIZE      CYLS        HEAD   PRECOMP   LANDZ      SEC       MODE

PRIMARY MASTER    :  AUTO 	0 	0 	0 	0 	0 	       0	       NORMAL

PRIMARY Slave 	    :  AUTO 	0 	0 	0 	0 	0 	       0          AUTO

Secondary MASTER  :  AUTO 	0 	0 	0 	0 	0 	       0	         AUTO

Secondary Slave 	    :  AUTO 	0 	0 	0 	0 	0 	       0          AUTO

Drive A 	:   None

Drive B 	:   None

Video 	    :   EGA/VGA

Halt On    :   None

Multi IO Defaults

| Onboard FDC Controller : Disabled Onboard Serial Port 1 : 3F8/IRQ4 Onboard Serial Port 2 : 2F8/IRQ3 Onboard Serial Port 3 : Disabled Onboard Serial Port 4 : 2E8/IRQ10 Onboard IR Controller : Disabled Onboard Parallel Port : 378/IRQ7 Parallel Port Mode PS/2 mouse function : Enabled : SPP | funworld I/O address : 210h ( for serial TS - Controller change port3 to 3E8/IRQ3 ) |
| --- | --- |

Save & Exit SETUP:		Yes by pressing "Z"

# Text boxes

Socket 7 Processor with fan

Battery

Keyboard

COM A-D

Dallas Dongle